## Slide 1: Meeting Presentation: Reinforcement learning of action sequences in table football
Alexandros Kyrloglou
Promotor: Wannes Meert Guidance: Jens Bürger
Wen-Chi Yang

## Slide 2: Context & Motivation
Development of robotic foosball.
From theoretic RL implementation to real life robotic implementation.
MDP: {S, A, T, R, p(s0), 𝛾}
  S (continuous)
  A (continuous/discrete)
  R(S)

## Slide 3: Similar Research
Foosball:
Kicker: mainly shooting, RL to Real
EPFL: Decision Tree, Control Engineering
Table Tennis:
ML agent project/competition: similar interaction with the ball
Robotic Arm:
Assembly Tasks: Curriculum Approach, Sim to Real
Robust Continuous Control
Robotic Soccer:
Opponent Modeling

## Slide 4: Methodology
Continuous environment
Possible solutions:
Discretization of state-action space
Function approximation for value and/or policy function.
On-policy (PPO) vs Off-policy (SAC)
PPO:
Faster convergence
Computationally cheaper
Low dimensional
SAC:
Data efficient
Exploration
Sparse rewards
Less Hyperparameter tuning

## Slide 5: Problem statement
Goal is passing between controllable players.
Types of passes:
  Ball control (tick-tacking)
  Forward Pass 5 to 3 player:
    Static opponent: Non-factor, single position
    Dynamic opponent: rhythmic, random static, random movement
    Enemy agent
  Adding Noise
  Transfer: Mirror, Other rod.
Metrics: speed of ball, time to completion, success rate (opponent type).

## Slide 6: Foosball as an RL environment
CURRENTLY:
  Observations
    Only Necessary Rods: (x, θ)
    Ball: (x, y)
  Actions
    Translations
    Rotations
    Discrete on/off
  Reward
    Denser (Reward shaping)

## Slide 7: Foosball as an RL environment
INITIAL IDEA:
  Observations
    Rods: (x1, θ1, x2, θ2, x3, θ3, x4, θ4)
    Ball: (x, y)
  Actions
    4 Translations
    4 Rotations
  Reward
    Sparse (only goal)

## Slide 8: Current Progress
Successes:
Environment setup: model, physics, controls
Defining RL environment: ML-agents, Unity, training
Simple task: tick-tack
Complex task setup
Experimenting on:
Observations:
  Rod / player
  Global / Relative coordinates
Actions:
  Discrete choice
Agent setup:
  Single / multi agent
  PPO / SAC
Reward Function:
  Shaping
  Curriculum Learning

## Slide 9: Reward Structure
Both Agents:
  Ball in zone (±0.003/action)
Pass Agent:
  Touch Passer (+5)
  Touch Receiver (+20)
  Trigger (±10)
  Target (+15)
  Loose ball (-10/-20)
Receive Agent:
  Touch Receiver (+30)
  On Target (+0.01/frame, +10)
  Loose ball (-5/-30)
lane
trigger
target
Min
Max

## Slide 10: Thank you
References:
De Blasi, Stefano & Klöser, Sebastian & Müller, Arne & Reuben, Robin & Sturm, Fabian & Zerrer, Timo. (2020). KIcker: An Industrial Drive and Control Foosball System automated with Deep Reinforcement Learning. 10.13140/RG.2.2.19201.28003. EPFL Robotic foosball: https://actu.epfl.ch/news/a-robot-to-beat-humans-at-foosball/ Aratrika Basu & Jayantraj Coimbatore Selvakumar & Justin Fu “Learning to play Table Tennis using Multi-agent Reinforcement Learning”. L. Leyendecker, M. Schmitz, H. A. Zhou, V. Samsonov, M. Rittstieg and D. Lütticke, "Deep Reinforcement Learning for Robotic Control in High-Dexterity Assembly Tasks - A Reward Curriculum Approach," 2021 Fifth IEEE International Conference on Robotic Computing (IRC), Taichung, Taiwan, 2021, pp. 35-42, doi: 10.1109/IRC52146.2021.00012. Yuan Zhang, Jianhong Wang, Joschka Boedecker “Robust Reinforcement Learning in Continuous Control Tasks with Uncertainty Set Regularization” Jordan Boyd-Graber, Kevin Kwok, He He “Opponent Modeling in Deep Reinforcement Learning”